## Slide 1: Business Data Communications & Networking
Chapter 1
Introduction to Data Communications

## Slide 2: Outline
Why Networks are Important
Basic Network Components
Network Types
Network Layers
Network Standards
Trends
Implications for Management

## Slide 3: Why Networks are Important
Data, data, data!
Modern organizations rely on the efficient transmission of data
Enables distributed systems, real-time communication, electronic commerce, social media, and the Web

## Slide 4: Why Networks are Important
By 2016, Cisco estimates that over 3,000 Petabytes of information will be transferred over the Internet DAILY!
Netflix accounts for around 1/3 of primetime downstream traffic
During the holiday 2013 season, Amazon sold an average of 426 items per SECOND!
As of 2012, every DAY on Facebook there are:
  2.7 Billion Likes
  300 Million Photos uploaded
  >500 Terabytes of data transmitted
Notes: http://www.cisco.com/c/en/us/solutions/collateral/service-provider/ip-ngn-ip-next-generation-network/white_paper_c11-481360.pdf
http://variety.com/2014/digital/news/netflix-youtube-bandwidth-usage-1201179643/
http://www.theverge.com/2013/12/26/5245008/amazon-sees-prime-spike-in-2013-holiday-season
http://www.cnet.com/news/facebook-processes-more-than-500-tb-of-data-daily/

## Slide 5: Data Communications
Data Communications is the movement of computer information from one point to another by means of electrical or optical transmission systems
Telecommunications is a broader term and includes the transmission of voice and video (images and graphics) as well as data and usually implies longer distances

## Slide 6: Basic Network Components
Client is a user device to access network and receive data from server
  e.g., desktops, laptops, tablets, cell phones, etc.
Server is a device that stores and transmits data to a client
  e.g., Web server, mail server, file server
Circuit is a pathway or connection between client and server
  e.g., copper wire, fiber optic cable, wireless

## Slide 7: Basic Network Components

## Slide 8: Types of Networks
One way to categorize networks is in terms of geographic scope:
Local Area Networks (LANs)
  Covers a small, clearly defined area
  Might contain a single floor or work area or single building
  When LANs use wireless circuits, they are called Wireless Local Area Networks (WLAN)
Backbone Networks (BNs)
  High-speed networks connecting other networks together
  May span hundreds of feet to several miles
Wide Area Networks (WANs)
  Largest geographic scope
  Often composed of leased circuits
  May spans hundreds or thousands of miles

## Slide 9: Types of Networks

## Slide 10: Types of Networks
Another way to categorize networks is in terms of access:
Intranet
  A network (often a LAN) that uses the Internet technologies to share information within an organization
  Open only those inside the organization
  e.g., employees accessing budgets, calendars, and payroll information available through the organization’s intranet
Extranet
  A network that uses the Internet technologies to share information between organizations
  Open only those invited users outside the organization
  Accessible through the Internet
  e.g., suppliers and customers accessing the inventory information of a company over an extranet

## Slide 11: Network Models
Network Models divide communication functions into layers
  Open Systems Interconnection Reference Model (OSI model)
  Internet Model (or TCP/IP model)
In practice, the Internet Model “won”

## Slide 12: Network Models
Application
Presentation
Application
Session
Transport
Network
Data Link
Transport
Network
Data Link
Physical
Physical
Some versions of the Internet model combine layers.
Transport + Network = Internetwork
Data Link + Physical = Hardware
Hardware
Internetwork
OSI Model
Internet Model
Application

## Slide 13: Network Models
Protocol defines the language of transmission
  It specifies the rules, functionality, and messages for communication at the layer
Protocol Data Unit (PDU) contains layer-specific information necessary for a message to be transmitted through a network
  Each layer adds a PDU
  PDUs act like nested envelopes
  Encapsulation occurs when a higher level PDU is placed inside of a lower level PDU

## Slide 14: Network Models
Layer
Purpose
Example Protocols / Standards
PDU
5. Application
User’s access to network, software to perform work
Packet (or Data)
4. Transport
TCP, UDP
Segment
3. Network
Deciding where the message goes
Addressing
Routing
IP, ICMP
Packet
2. Data Link
Move a message from one device to the next
Controls hardware
Formats the message
Error checking
Ethernet
Frame
1. Physical
Transmits the message
100BASE-T, 802.11n
HTTP, SMTP, DNS, FTP, DHCP, IMAP, POP, SSL
End-to-End Management
Link application layer to network
Segmenting and tracking
Flow control

## Slide 15
 | Sender | PDU | Receiver
Application |  | Packet | 
Transport |  | Segment | 
Network |  | Packet | 
Data Link |  | Frame | 
Physical |  |  | 
TCP
HTTP
Request
Ethernet
IP
TCP
HTTP
Request
HTTP
Request
IP
TCP
IP
TCP
HTTP
Request
Ethernet
Ethernet
IP
TCP
HTTP
Request
IP
TCP
HTTP
Request
TCP
HTTP
Request
HTTP
Request
HTTP
Request

## Slide 16: Network Models
Advantages of Layers
  Networking functionality is modular and the software/hardware at any layer can be more easily substituted
    E.g., substitute wired for wireless at the physical layer
  Easier to troubleshoot or make changes to one layer at a time
  Application developers only need to worry about the application layer in their programs
Disadvantages of Layers
  Inefficient because the encapsulation/de-encapsulation at each layer requires processing
  Inefficient because encapsulation in a PDU increases overhead at each layer

## Slide 17: Network Standards
Standards ensure that hardware and software from different vendors work together and “speak the same language”
De jure standards
  Formalized by an industry or government body
  e.g. HTTP, IEEE 802.3, 802.11n
De facto standards
  Widely accepted, but not formalized
  e.g. Microsoft Windows
  Often become de jure standards eventually

## Slide 18: Network Standards
De jure standardization process
Specification
Acceptance
Identification of Choices

## Slide 19: Network Standards
Common Network Standards

## Slide 20: Trends
Bring your own device (BYOD)
  Huge demand for employees to connect their personal smartphones, tablets, and other devices to organizational networks
  Security challenges
  Who is responsible for support?

## Slide 21: Trends
The Web of Things
  Everything connects to the network!
    e.g., cars, refrigerators, thermostats, shoes, doors, etc.
  Networks need to support the increased demands of these devices

## Slide 22: Trends
Massively Online
  Not just multiplayer online games
  Massive open online courses (MOOC)
  Millions online participating is social media and other activities
  Will require greater network infrastructure

## Slide 23: Implications for Management
Networks and the Internet change (almost) everything
Today’s networking is driven by standards
As network demand increases, so will storage demands