## Slide 1: Business Data Communications & Networking
Chapter 3
Physical Layer

## Slide 2: Outline
Circuits and Data Flow
Multiplexing
Media
Digital Transmission of Digital Data
Analog Transmission of Digital Data
Digital Transmission of Analog Data
Implications for Management

## Slide 3: Physical Layer
Layer 1 in the Internet model
Focus on transmission over circuits
Types of Circuits
  Physical circuits connect devices & include wires
  Logical circuits refer to the transmission characteristics of the circuit
Transport
Network
Data Link
Physical
Application
Internet Model

## Slide 4: Circuits
Circuit Configuration
  Point-to-Point circuits include most wired connections today
  Multipoint circuits are most commonly used in wireless today
Shared circuits (multipoint) are less expensive

## Slide 5: Data Flow
Data flows in one direction
Data flows both directions, but only one at a time
Data flows simultaneously in both directions

## Slide 6: Multiplexing
Divide high-speed circuit into several slower (logical) circuits
Main advantage is cost
Categories of multiplexing
  Frequency/Wavelength
  Time

## Slide 7: Multiplexing
Frequency Division Multiplexing (FDM)
  Creates “channels” from larger frequency band
  Guardbands separate channels to prevent interference

## Slide 8: Multiplexing
Wavelength Division Multiplexing (WDM)
  A variant of FDM used in fiber optic circuits
  Makes use of multiple light wavelengths (colors) to divide circuit into channels
  Dense WDM can divide circuit into more than 100 channels per fiber each transmitting at 10 Gbps

## Slide 9: Multiplexing
Statistical Time Division Multiplexing (STDM)
    A variation of TDM
    Designed to reduce idle time slots by allocating slots based on statistical network usage
    Disadvantages
      Potential time delays when actual usage does not match statistically allocated time slots
      Additional logical addressing requirements
Time Division Multiplexing (TDM)
  Circuit is divided by devices taking turns
  In traditional TDM, all have equal turns
  More efficient than FDM, but may have idle time slots

## Slide 10: Multiplexing
Inverse multiplexing
  Combines many low-speed circuits into one high-speed circuit
  e.g., two T-1 lines multiplexed (creating a capacity of 2 x 1.544Mbps = 3.088 Mbps)

## Slide 11: Media
Physical matter used to carry voice or data transmissions
Guided media – transmission flows along physical medium
Wireless (Radiated) media - transmission flows through the air

## Slide 12: Guided Media
Twisted-pair (TP) cable
  Insulated pairs of wires bundled together
  Wires twisted to reduce electromagnetic interference
  Some times use additional shielding (STP)
  Commonly used for telephones, LANs
  Characteristics
    Price – inexpensive
    Distance – typically up to 100m
    Use - Telephones, LANs
Notes: License: Public Domain
URL: http://commons.wikimedia.org/wiki/File:UTP_cable.jpg
Author: Baran Ivo

## Slide 13: Guided Media
Coax cable
  Has a single copper core, plus outer insulation, shielding, and inner insulation
  Less prone to interference
  Characteristics
    Price - inexpensive (but more costly than TP)
    Distance - up to 2 km (1.2 miles)
    Use: Cable TV / Internet

## Slide 14: Guided Media
Fiber optic cable
  Optical core made of glass or plastic
  Data transmitted using light from lasers or LEDs
  Resistant to interference and corrosion
  Extremely fast data rates
  Characteristics
    Price: Expensive
    Distance: 500m – 100km
    Use: Trunk line / Backbone, long distance circuits (e.g., undersea cables)
Notes: License: CC By
URL: http://commons.wikimedia.org/wiki/File:MultimodeFiber.JPG
Author: Hhedeshian

## Slide 15: Guided Media
Fiber optics
  Multimode (about 50 micron core)
  Graded index multimode
  Single mode (about 5 micron core)

## Slide 16: Wireless Media
Radio
  Wireless transmission of electrical waves through air
  Each device on network has a radio transceiver operating at a specific frequency range
  Enables mobile network communication
  Characteristics
    Distance: depends on frequency and power
    Use: Wireless LANs, cellular and cordless phones, baby monitors

## Slide 17: Wireless Media
Microwave
  High-frequency radio communication
  Requires line of sight which may require large antennas and towers
  Affected by weather
  Characteristics
    Distance: ~60 km (due to curvature of earth
    Use: Trunk line / Backbone, long distance
Satellite
  Special form of microwave communication
  Long distance leads to propagation delays

## Slide 18: Media
Factors to consider in media selection
  Type of network
  Cost
  Transmission distance
  Security
  Error rates
  Transmission speeds

## Slide 19: Digital vs. Analog Data
Digital transmission involves discrete binary values (i.e., 0 or 1)
Analog transmission involves continuous waves

## Slide 20: Digital Transmission of Digital Data
Coding scheme needed to ensure sender and receiver understand messages (e.g., ASCII, Unicode, etc.)
A character is represented by a group of bits
Total |  | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
255 |  | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1

## Slide 21: Digital Transmission of Digital Data
Transmission modes
  Parallel: multiple bits transmitted simultaneously
0
1
0
1
0
1
1
0

## Slide 22: Digital Transmission of Digital Data
Transmission modes
  Serial: bits are transferred sequentially, one at a time
0
1
0
1
0
1
1
0

## Slide 23: Digital Transmission of Digital Data
Sender and receiver must agree upon:
  Set of symbols
    How bits are encoded as voltages or light pulses
    e.g., +5V might be encodes as a “1”
  Symbol rate
    How often symbols are sent
    e.g., with a symbol rate of 64 kilohertz (kHz), a symbol is sent every 1/64,000 of a second

## Slide 24: Digital Transmission of Digital Data
Five types of signaling techniques
  Unipolar - voltage is 0 or positive representing binary bits (in some circuits, 0 and negative voltage could be used)

## Slide 25: Digital Transmission of Digital Data
Five types of signaling techniques
  Bipolar NRZ - voltage is positive or negative, but not zero
    Fewer errors than unipolar because signals are more distinct

## Slide 26: Digital Transmission of Digital Data
Five types of signaling techniques
  Bipolar RZ - voltage is positive or negative, returning to zero between each bit
    Fewer synchronization errors than bipolar NRZ

## Slide 27: Digital Transmission of Digital Data
Five types of signaling techniques
  Bipolar AMI - voltage is 0, positive, or negative, returns to zero between each bit, and alternates between positive and negative voltage

## Slide 28: Digital Transmission of Digital Data
Five types of signaling techniques
  Manchester - voltage is positive or negative and bits are indicated by a mid-bit transition

## Slide 29: Analog Transmission of Digital Data
Telephone system built for analog data
  Electrical signals mimic sound waves (i.e., voice)
  Analog transmissions take on range of values (vs. discrete values of digital transmissions)
  Need a modem (modulator/demodulator) to convert from analog to digital and vice versa

## Slide 30: Analog Transmission of Digital Data
Three characteristics of waves
  Amplitude: height of wave (decibels)
  Frequency: waves per second (hertz)
    Wavelength is the inverse of frequency
  Phase: wave direction (degrees) or the point at which the wave begins

## Slide 31: Analog Transmission of Digital Data
Carrier wave is basic wave transmitted through a circuit
Modulation is the modification of a carrier wave’s fundamental characteristics in order to encode information
Three ways to modulate a carrier wave:
  Amplitude Modulation (AM) or Amplitude Shift Keying (ASK)
  Frequency Modulation (FM) or Frequency Shift Keying (FSK)
  Phase Modulation (PM) or Phase Shift Keying (PSK)

## Slide 32: Analog Transmission of Digital Data
Amplitude Modulation
Frequency Modulation
Phase Modulation

## Slide 33: Analog Transmission of Digital Data
Symbol: One or more modifications to a carrier wave used to encode data
Can send 1 bit by defining two different symbols (e.g., amplitudes, frequencies, etc.)
Can send multiple bits by defining more than two symbols
  Need more complicated information coding schemes
  1 bit of information  2 symbols
  2 bits of information  4 symbols
  3 bits of information  8 symbols
  n bits of information  2n symbols

## Slide 34: Analog Transmission of Digital Data
Two-bit Amplitude Modulation
  With 4 levels of amplitude defined as symbols, 2 bits can be transmitted per symbol

## Slide 35: Analog Transmission of Digital Data
Data rate (or bit rate) is the number of bits transmitted per second
Symbol rate: number of symbols transmitted per second
Data rate = symbol rate × (# bits/symbol)
Example
  Symbol rate = 16,000 symbols/sec
  #bits/symbol = 4 bits/symbol
  Data rate = 16,000 symbols/sec × 4 bits/symbol
  = 64,000 bits/sec = 64Kbps

## Slide 36: Digital Transmission of Analog Data
Codecs (COde, DECode) is a device or software that converts an analog signal (e.g., voice) into digital form and the reverse
Pulse-Code Modulation (PCM) converts analog to digital by:
  Sampling the analog signal at regular intervals
  Measuring the amplitude of each sample
  Encoding (quantizing) the amplitude as binary data
Quantizing Error is the difference between the original analog signal and the approximated, digital signal
Reducing quantizing error can be done by:
  Sampling more frequently
  Using more levels of amplitude in encoding

## Slide 37: Digital Transmission of Analog Data

## Slide 38: Implications for Management
Digital cabling tends to be least expensive and most reliable
Data and voice networks continue to converge
Wired networks remain more secure and reliable than wireless