## Slide 1: Business Data Communications & Networking
Chapter 6
Network Design

## Slide 2: Outline
Network architecture components
Traditional network design
Building-block network design
  Needs analysis
  Technology design
  Cost assessment
Implications for management

## Slide 3: Network Architecture Components
Local area network (LAN) – Ch. 7
Building backbone network (or distribution layer) – Ch. 8
Campus backbone (or core layer) – Ch. 8
Data center – Ch. 7
Enterprise edge
  Wide area network (WAN) – Ch. 9
  Internet access – Ch. 10
  e-commerce edge – Ch. 7 & 11

## Slide 4: Network Architecture Components

## Slide 5: Traditional Network Design
A structured systems analysis and design process
Network analysis phase includes:
  Meeting with users to determine the needs and applications
  Estimating data traffic on each part of the network
During the network design phase, the logical and physical networks are designed and circuits and hardware selected
Implementation phase is the building and implementing of the network
Analysis Phase
Design Phase
Implementation Phase

## Slide 6: Traditional Network Design
Pros
  Useful for static and slowly evolving networks
Cons
  Costly
  Time consuming
  This approach may not be adequate today due to:
    Rapid changes in technology
    Escalating network traffic demands
    Decrease in hardware costs and increase in staff costs

## Slide 7: Building Block Network Design
Uses a few standard components to simplify design and reduce costs
Iterative design phases
  Needs analysis
    Understand current and future network needs (users and applications)
  Technology design
    Examine available technologies to determine which meet or exceed needs
    If needs are difficult to estimate, build higher capacity
  Cost assessment
    Evaluate financial costs of technology
Needs Analysis
Technology Design
Cost Assessment

## Slide 8: Needs Analysis
Why is the network needed?
  Performance issues may exist
  The organization may be standardizing
  Hardware may need replacement
What users and applications must be supported?
Goals differ depending on the network component
  LAN and BN typically are built with organizational ownership and are often built with excess capacity
  WANs rely more on leased equipment and circuits are typically designed at or near capacity with organizations leasing additional circuits as required
Needs Analysis

## Slide 9: Needs Analysis
Baselines
  Create metrics of current operations to compare design requirements against
  Baselines may include
    Sequence of operations
    Processing times
    Work volumes
    Existing costs
    Existing user/management needs
Needs Analysis

## Slide 10: Needs Analysis
Break down the network into architectural components
  Evaluate all seven components
  Often easiest to start with WANs
  Geographic scope of network
Review the existing and expected applications that will use the network
  Identify hardware and software requirements for these applications
  Identify protocols used by applications
Needs Analysis

## Slide 11: Needs Analysis
Identify and assess network users
  Some users may have very different needs
  How many of each type of user?
Categorize network requirements
  Mandatory
  Desirable
  Wish-list
Needs Analysis

## Slide 12: Needs Analysis
Deliverable: Logical network design
Needs Analysis

## Slide 13: Technology Design
Development of a physical network design (or set of possible designs)
Design includes clients, servers, circuits, and networking devices (routers, gateways, access points, switches, etc.)
What new hardware needs to be purchased?
Can the existing equipment be upgraded?
Technology Design

## Slide 14: Technology Design
Designing clients and servers
  Specify of the devices needed in standard units
  “Typical” users are allocated base-level clients
  “Advanced” users are allocated advanced clients
  Servers are similarly allocated based on application needs
  Definitions of “typical” and “advanced” change as hardware costs fall, and capabilities increase
Technology Design

## Slide 15: Technology Design
Designing circuits
  Capacity planning is the estimation of circuit size and type required for each network architecture component
  Circuit loading is an assessment of the amount of data transferred across a circuit (currently or in the future)
Technology Design

## Slide 16: Technology Design
Estimating circuit traffic
  Average traffic vs. peak traffic
  Designing for peak traffic is ideal
Estimating message volume
  Count messages sent in the current network and multiply by the expected growth rate
Precision may not be the major concern
  Obtaining precise estimates is difficult and expensive
  Standard circuit speeds “stair step”
  Traffic typically increases more than anticipated
Technology Design

## Slide 17: Technology Design
Should network designers plan for excess capacity?
  Upgrading costs 50-80% more than designing higher capacity time
  Very few complaints about overcapacity
Most organizations intentionally overbuild
The turnpike effect occurs when traffic increases faster than forecasts
  When networks are efficient and fast, users will use them more frequently
  Most networks designed with excess capacity end up using overcapacity within 3 years
Technology Design

## Slide 18: Technology Design
Network Design Tools
  Modeling
    Users create diagrams of existing or proposed networks
  Discovery
    Some tools can automatically create network diagrams by examining existing network
  Simulation
    A mathematical technique used to model the behavior of a network under real conditions
    Simulates applications and users generating traffic and responding to messages
    May highlight potential problems
Technology Design

## Slide 19: Technology Design
Deliverable: One or more physical network designs
  Multiple designs may be created to highlight tradeoffs between performance and cost
  Design of circuits and networking devices
  Designs for new/upgraded clients and servers
Technology Design

## Slide 20: Technology Design
Technology Design

## Slide 21: Cost Assessment
Cost Assessment
Financial analysis of the various technology design alternatives
Complex process that requires analysis of many factors:
  Circuit costs (cabling and installation)
  Internetworking devices (switches and routers)
  Hardware costs (clients, servers, power supplies)
  Software costs (operating systems, application software and middleware)
  Network management and maintenance costs
  Operations costs to run the network
  WAN and Internet circuits

## Slide 22: Cost Assessment
Cost Assessment
Request for proposal (RFP)
  Detailed specification of equipment, software, and services desired from vendors
  Typically used in large network purchases
  May include timeline and evaluation criteria for proposals
Allows the organization to evaluate offerings from different vendors
Multi-vendor proposals
  May provide better performance
  May be less expensive
  May be more difficult to manage

## Slide 23: Cost Assessment
Cost Assessment
Selling the proposal to management
  Understand that networks, data centers, and most information technology is viewed as a cost center
  Make a business case by focusing on organizational needs and strategy
  The importance of network speed, reliability, and security are easy for non-technical users to understand
  Avoid focusing on technical details and jargon

## Slide 24: Cost Assessment
Cost Assessment
Deliverables
  Finalized RFP that is sent to vendors
  Revised technology design with detailed specifications including exact products and costs
  Business case for the network design

## Slide 25: Implications for Management
Network design increasingly relies on standardized technologies and a building-block design
The cost of hardware, software, and circuits is less expensive in the long-run than human resources to manage network
  This may make more expensive hardware that is easier to manage a better long-term financial decision
Network usage continues to grow and designing networks with extra capacity is less expensive than upgrading later